## Slide 1: Non-Preemptive Buffer Management for Latency Sensitive Packets
Moran Feldman
Technion
Seffi Naor
Technion

## Slide 2: Outline
Model and motivation
Prior art and our results
Focusing on results:
  Lower bound for Unrestricted Model
  Deterministic algorithm for Integral Valued Model
  Randomized algorithm for Real Valued Model
Open problems

## Slide 3: Motivation
Consider a path in a communication network:
Router
Router
Router
A packet going through the path often has a deadline.
The deadline refers to the arrival of the packet to its destination.
An online model of a router must deal with these deadlines:
  Traditional models assume a deadline for leaving the router.
  A new model (proposed by Fiat, Mansour and Nadav [SODA 2008]), associates each packet with a value that diminishes over time.

## Slide 4: The Model
2
Our model is based on the model of Fiat et. al.
Router’s queue
Unlimited size
Packets
Continues, starting at time 0
Packets arrive at fractional times and are transmitted at integral ones.
Arrive online, each has an associated value w(d).
Must be rejected or accepted immediately.
Time
At each integral time the first packet of the queue is transmitted. Its revenue is w(d) minus the delay it suffered in the queue.
4
3

## Slide 5: Competitive Ratio
Standard performance measure for online algorithms.
Notation
I – An instance of an online problem.
ALG(I) – The value of an online algorithm ALG on I.
OPT(I) – The value of the optimal offline algorithm on I.
For Deterministic Algorithms
For Randomized Algorithms
Against oblivious adversary.
Other adversary types also exist.
Randomization often improves the achievable competitive ratio.

## Slide 6: Known and New Results
Sub models
Unrestricted model – A packet can have any positive value.
Real valued model – A packet can have any value ≥ 1.
Integral valued model – A packet can have any positive integral value.
 |  | Unrestricted Model | Real Valued Model | Integral Valued Model
Deterministic | Lower bound | 3 | 3 | 3
 | Upper bound | - | 4.24 | 4.24
Randomized | Lower bound | φ ≈ 1.618 | φ ≈ 1.618 | φ ≈ 1.618
 | Upper bound | - | 4.24 | 4.24
Known results inferred from Fiat et. al.
 |  | Unrestricted Model | Real Valued Model | Integral Valued Model
Deterministic | Lower bound | ∞ (3) | φ3 ≈ 4.236 (3) | 4 (3)
 | Upper bound | - | 4.24 | 4 (4.24)
Randomized | Lower bound | ∞ (φ) | 4 (φ) | 4 (φ)
 | Upper bound | - | 4 (4.24) | 4 (4.24)
New results appear in red.

## Slide 7: Unrestricted Model – Lower Bound
Consider any algorithm ALG and a constant c.
Our job: Show that ALG is not c-competitive.
Plan of Adversary
For i = 1 to 2c do:
Give ALG a packet of value (1/2c)2c+1-i.
If the probability that ALG accepted any packet, so far, is less than i/2c, terminate.
Give ALG a packet of value 1.
Proof Idea
Packets have exponentially increasing values, but all values are at most 1, so only one packet gives revenue.
ALG must accept each packet with some probability.
OPT accepts with probability 1 the last packet.

## Slide 8: The Dual-Fitting Method
Offline Primal Program
y(d,t) – Indicates whether packet d was transmitted at time t.
w(d) – The value of packet d.
a(d) – The time when packet d arrived.
Remark
The LP contains no FIFO constraint because this is no constraint from the offline point of view.
Dual

## Slide 9: The Dual-Fitting Method (cont.)
Offline Dual Program
Method
Every dual solution is an upper bound on OPT.
To show that an algorithm is c-competitive we do the following:
  Consider any input sequence σ.
  Calculate the revenue Rσ of the algorithm on σ.
  Find a dual solution of value Dσ for σ.
  Prove that Dσ/Rσ ≤ c.
Dual

## Slide 10: Deterministic Reduction to Simple Inputs
Definition
An input sequence is simple if all packets in it arrive before time 1.
Reduction
If there is a deterministic R-competitive algorithm A on simple input sequences, then there exists a deterministic R-competitive algorithm B on all input sequences.
Definition of B
B’s Input:
A’s Input:
1. B simulates A and maps each input packets to A’s input.
2. Map each packet to time before time 1, and increase its value by the number of transmissions so far.
5
5
3
3
0
1
2
3
4
5
7
8
3. Reset the algorithm when the queue empties.

## Slide 11: Deterministic Reduction to Simple Inputs (cont.)
Why Does It Work?
Let an interval be the time between two consecutive resets.
B (and A) transmit packets at all integral times in an interval.
Moving packets to earlier time:
  Does not effect the transmission times.
  Increase the delay that the packets suffer.
Increasing the value of the packets counter the additional delay.
0
1
2
3
5
5
3
3
7
8

## Slide 12: Deterministic Algorithm for Integral Simple Inputs
Algorithm (NDT)
Let Q be the number of packets in the router’s queue.
Accept a new packet d if and only if w(d) ≥ 2Q + 1.
Remark
The algorithm also works for general integral inputs, although it is more difficult to show that.
Reduction
Assume that if a packet d is accepted, then its value is exactly 2Q+1.
Proof
This is the lowest value that will get the packet accepted.

## Slide 13: Analyzing NDT
Assume k packets have been received:
Value for the Algorithm
Packet Value
Delay
Assignment to the Dual LP
zd = 0
xt = max{2k - t, 0}
Value of solution:
The competitive ratio of NDT is:

## Slide 14: Randomized Reduction to Simple Inputs
Difficulty
The previous reduction does not work for randomized algorithms:
If we restart each time the queue empties, the simulated algorithm A will face a non-oblivious adversary.
If we do not restart, the algorithm will not necessarily have a packet to send at each integral time of an interval.
Definition
A randomized algorithm is good if at all times an external observer can give a number P such that:
The algorithm has either P or P+1 packets in its queue.
P does not depend on the random decisions of the algorithm.
Remark
In a sense, a good algorithm is a randomized algorithm with minimal randomness.

## Slide 15: Randomized Reduction to Simple Inputs (cont.)
Idea
We reset A’s simulation after every integral time in which we might not have a packet to transmit.
This ensures that the queue is empty after every reset. Either:
  The queue was empty before the integral time.
  The last packet was sent during the integral time.
A faces an oblivious adversary.
  The reduction does not depend on A’s randomized decisions.
The algorithm transmits at each integral time between resets.
Objective
Make the previous reduction work for good randomized algorithms.

## Slide 16: Randomized Algorithm for Real Valued Simple Inputs
Algorithm (RNDT)
Let Q be a random variable of the size of the queue.
Keep the invariant Q = E(Q)  or Q = E(Q) .
Accept a new packet d with probability:
To keep the invariant, true acceptances probability depends on the random variable Q.
d first packet | w(d) ≤ 2E(Q)+0.5 | 2E(Q)+0.5 ≤ w(d) ≤ 2E(Q)+2.5 | w(d) ≥ 2E(Q)+2.5
½ | 0 | w(d) / 2 – 0.25 – E(Q) | 1
Reduction
Let Ef be the final value of E[Q]. No packet had value over 2Ef + ½.
Proof
Implied by the acceptance probabilities.

## Slide 17: Analyzing RNDT
Value for the Algorithm
First Packet
A packet of value 2E[Q]+0.5+ε is accepted to ε extent.
Assignment to the Dual LP
zd = 0
xt = max{2Ef + 1.5 - t, 0}
Value of solution:
The competitive ratio of RNDT is:

## Slide 18: Open Problems
Adversary that draws from a malicious distribution.
  Competitive analysis provides too pessimistic a view.
  Classic queuing theory analyzes Poisson distributed source.
  Provides a middle ground between the two approaches.
A sub-model where all values above some constant c are allowed.
  Generalizes the unrestricted and real-valued models.
  The constant c represent the ratio between the shortest deadlines and the speed of the network.
  The main question is finding the relation between c and the competitive ratio.

## Slide 19
Questions?